## Slide 1: Day 13
Fundamental Problems in Mobile Robotics

## Slide 2: Fundamental Problems
Chapter 2 of Dudek and Jenkin begins:
  "Before delving into the harsh realities of real robots..."

## Slide 3: A Point Robot
represents a mobile robot as a point in the plane*
the point P fully describes the state of the robot
  called pose or configuration
robot motion causes the state to change
  i.e., if the robot moves from P to Q then its state changes from

## Slide 4: Free Space and Obstacles
the set of valid poses is called the free space Cfree of the robot
the invalid poses are obstacles
obstacle
obstacle
obstacle
obstacle
freespace
point
robot
obstacle

## Slide 5: Path Planning
is it possible for the robot to move to a goal configuration while remaining in Cfree ?
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal

## Slide 6: Path Planning Using Bugs
bug algorithms assume:
  point robot
  known goal location
  finite number of bounded obstacles
  robot can perfectly sense its position at all times
  robot can compute the distance between two points
  robot can remember where it has been
  robot can perfectly sense its local environment
  robot can instantaneously change direction

## Slide 7: Bug Zero
assumes a perfect contact sensor
repeat
  head towards goal
  if goal is reached then stop
  if an obstacle is reached then follow the boundary until heading towards the goal is again possible

## Slide 8: Bug Zero
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal
a right turning bug

## Slide 9: Bug Zero
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 10: Bug Zero
not guaranteed to reach the goal
obstacle
goal
start

## Slide 11: Bug One
assumes a perfect contact sensor
repeat:
  head toward goal T
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until returning to H and remember the point L (the leave point) closest to T from which the robot can depart directly towards T
      if no such point L exists then the goal is unreachable; stop
    move to L using the shortest boundary following path

## Slide 12: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 13: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 14: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 15: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 16: Bug Two
Bug Two uses a line, called the m-line, from the start point to the goal
  textbook calls the m-line the direct path
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 17: Bug Two
assumes a perfect contact sensor
repeat:
  head toward goal T along the m-line
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until the m-line is crossed at a leave point closer to the goal than H
      if no such point L exists then the goal is unreachable; stop
    leave the obstacle and head toward T

## Slide 18: Bug Two
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 19: Bug Two

## Slide 20: Bug One versus Bug Two
Bug One uses exhaustive search
  it considers all leave points before leaving the obstacle
Bug Two uses greedy search
  it takes the first leave point that is closer to the goal