## Slide 1
Jeff Edmonds
York University
Building a Computer From Sand
History of Computing
Layers of Abstraction
Building an AND Gate
AND/OR/NOT Circuits
Building a CPU
Parsing/Compiling
Abstract Data Types
Algorithms
AI

## Slide 2
Please feel free
to ask questions!
Notes: 2

## Slide 3
Yesterday,
this talk had no intro.
Fran’s lecture
inspired me
to make an engaging one.

## Slide 4
Do you know the basics
of how the things in your world
work?

## Slide 5
Do you know the basics
of how the things in your world
work?

## Slide 6
Do you know the basics
of how the things in your world
work?

## Slide 7
Do you know the basics
of how the things in your world
work?

## Slide 8
Do you know the basics
of how the things in your world
work?

## Slide 9
Do you know the basics
of how the things in your world
work?
<x,y>
 <y,x mod y>
GCD(a,b) = GCD(x,y)
Emergent Intelligence

## Slide 10
In the beginning:
<x,y>
 <y,x mod y>
GCD(a,b) = GCD(x,y)
And so it was.
Euclid said,
“ Let there be an algorithm for GCD”
Euclid (300 BC)
History of Computability
Low level
instructions
Emergent Complexity

## Slide 11
The Jacquard loom (1801) was one of the first programmable devices.
Weaves complex patterns in textiles.
Controlled by punched cards
This portrait of Jacquard was woven in silk on a Jacquard loom and required 24,000 punched cards to create (1839).
History of Computability
Low level
instructions
Emergent Complexity

## Slide 12
History of Computability
Charles Babbage’s Analytical Engine (1837)
  Memory
  An arithmetical unit,
  Conditional branching and loops,
Making it the first general-purpose computer.
Low level
instructions
Never actually worked

## Slide 13
Can every problem be computed?
Or are some Uncomputable?
One of his 23 influential open problems (1900)
Hilbert
Need to formally define
“Algorithm”
History of Computability

## Slide 14
Need to formally define
“Algorithm”
Turing
TM Computable
History of Computability
Halting
Problem
A problem is Computable
if it can be computed by a
Turing Machine. (1936)

## Slide 15
contents of tape
current state
Simple rules like these
produce complex patterns.
TM step:
Current state & cell content at head determines which rule to use giving:
  how cell contents changes
  how head moves
  how state changes
Time
Tape Cells
Low level
instructions

## Slide 16
Turing
Java
Computable
Are these definitions equivalent?
Church says “Yes”
All reasonable models of computation are equivalent
as far as what they can compute.
And within a polynomial in time
(except for Quantum Machines)
TM Computable
Though not intended to be practical, the Turing Machine hugely helped develop and understand the power and limits of mechanical computation.
Need to formally define
“Algorithm”
History of Computability
Emergent Complexity

## Slide 17
Turing
History of Computability
Helped breaking German code
Persecuted being gay.
And killed himself 

## Slide 18
History of Computability
Vacuum tubes made electronic computing possible
  Colossus (1943) 2,400 tubes, ENIAC (1946) 17,000 tubes
  5,000 characters per second
  $500,000 ($6 million with inflation).
  Tube failure (every two days, 15 min to locate)
  First “bug” was a moth in a tube.

## Slide 19
History of Computability
The first transistorised computer (1953)
Integrated circuits (1968)
Intel 4004 Microprocessors (1971)

## Slide 20: Layers of Abstraction
Low level
instructions
Emergent Complexity
Emergent Intelligence

## Slide 21: Layers of Abstraction
Low level
instructions
Emergent Complexity
Emergent Intelligence
The psychological profiling of a successful person is mostly the ability to shift levels of abstraction, from low level to high level.
To understand the detailed workings.
To understand the big picture.
Donald Kunth

## Slide 22: Layers of Abstraction
Low level
instructions
Emergent Complexity
The psychological profiling of a successful person is mostly the ability to shift levels of abstraction, from low level to high level.
To understand the detailed workings.
To understand the big picture.
To understand complex things in simple ways.
Donald Kunth
=

## Slide 23: Layers of Abstraction
Software developers view subsystems as entities with separate personalities, roles, and interactions,
not details of code.
vs
vs
It is hard to think of love in terms of the firing of neurons.

## Slide 25
Semiconductor

## Slide 27
Select between two alternatives A and B

## Slide 29
CPU
DRAM
I/O

## Slide 30
Loader
Linker
Memory Manager
I/O Controller
Process Manager
0x3c011001
0x34240028
0x20100226
0x00004020
0x00004820
0x3c011001
0x00290821
0x8c2a0000
0x51500006
0x21290004
0x292a0028
0x1540fffa
0x3c011001
0x34240031
0x20020004
0x0000000c
0x03e00008
boolean found = false; for (int i = 0; i < 10 && !found; i++) { found = (target == list[i]); }
la $a0, yes
addi $s0, $0, 550
add $t0, $0, $0
add $t1, $0, $0
lbl: lw $t2, list($t1)
beq $t2, $s0, ok
addi $t1, $t1, 4
slti $t2, $t1, 40
bne $t2, $0, lbl
la $a0, no
ok: addi $v0, $0, 4
syscall
jr $ra
Vision | Robotics | AI | HCI | DB | Sim | Bio | DC | QC
boolean found = list.contains(target);

## Slide 31: Lets do it again more slowly.

## Slide 32
Layers of Abstraction

## Slide 33
AND
y
x
z
Building an AND Gate
Electricity can’t jump large gap from Cathode to Plate.
It can jump from Cathode to Grid.
And if it starts flying, then it keeps going to the Plate.
Large jump happens iff power
to Grid AND to Plate

## Slide 34
AND
y
x
z
Building an AND Gate

## Slide 35
AND
y
x
z
Building an AND Gate

## Slide 36
Building an AND Gate

## Slide 37
Building an AND Gate
Four electrons in the outer ring.
Four holes in the outer ring.
Same as Carbon

## Slide 38
Building an AND Gate
Same as Carbon

## Slide 39
Building an AND Gate
Same as Carbon

## Slide 40
Building an AND Gate
Same as Carbon
Each Carbon/Silicon bonds with four others.

## Slide 41
Building an AND Gate
Same as Carbon

## Slide 42
Building an AND Gate
Same as Carbon

## Slide 43
Building an AND Gate
Electricity does not flow through it because all the electrons are happy.

## Slide 44
Building an AND Gate
Electricity flows through it because this extra electron
moves.
Dope it with what is one to the right in the periotic table, i.e. one extra electron.
Called N

## Slide 45
Building an AND Gate
Electricity flows through it because this extra hole
moves.
Dope it with what is one to the left in the periotic table, i.e. one extra hole.
Called P

## Slide 46
Building an AND Gate
Electricity flows from N to P
extra electron to extra hole.
N
P
Electricity does not flow from P to N
extra hole to extra electron

## Slide 47
Building an AND Gate
Once the electricity starts the electrons keep tunneling through!!!
N
P
N

## Slide 48
N
P
N
Building an AND Gate
Tunneling happens iff power across PN AND
across PNP

## Slide 49
Building an AND Gate
Tunneling happens iff power across PN AND
across PNP
AND
y
x
z

## Slide 50
Building an AND Gate
AND
y
x
z

## Slide 51
Building an AND Gate
AND
y
x
z

## Slide 52
And/Or/Not Circuits (acyclic)

## Slide 53
x3
x2
x1
OR
OR
AND
AND
OR
NOT
A circuit is a directed acyclic graph of and/or/not gates
0
1
0
An input X assigns a bit to each incoming wire.
The bits percolate down to the output wires.
0
0
0
0
0
1
  The Size of a circuit:
    is the number of gates.
    It relates to sequential computation time.
And/Or/Not Circuits (acyclic)

## Slide 54
x3
x2
x1
OR
OR
AND
AND
OR
NOT
  The depth of a circuit:
    is the length of the longest path from an input to an output.
    It indicates evaluation time.
    It relates to parallel computation time.
0
1
0
0
0
0
0
0
1
And/Or/Not Circuits (acyclic)

## Slide 55
5 volts
open
true
yes
1
0 volts
closed
false
no
0
And/Or/Not Circuits (acyclic)

## Slide 56
927310
= 3 100
+ 7 101
+ 2 102
+ 9 103
Decimal
10112
= 1  20
+ 1  21
+ 0  22
+ 1  23
Binary
9F7316
= 3 160
+ 7 161
+ 15 162
+ 9 163
Hexidecimal
And/Or/Not Circuits (acyclic)

## Slide 57: Add 2 n-bit numbers
* *
* *
* *
* *
* *
* *
* *
* *
* *
* *
* *
+
And/Or/Not Circuits (acyclic)

## Slide 58: Add 2 n-bit numbers
* *
*
* *
* *
* *
* *
* *
* * *
* *
* *
* *
* *
+
And/Or/Not Circuits (acyclic)

## Slide 59: Add 2 n-bit numbers
* *
*
* *
* *
* *
* *
* * *
* * *
*
* *
* *
* *
* *
+
And/Or/Not Circuits (acyclic)

## Slide 60: Add 2 n-bit numbers
* *
*
* *
* *
* *
* * *
* * *
*
* * *
*
* *
* *
* *
* *
+
And/Or/Not Circuits (acyclic)

## Slide 61: Add 2 n-bit numbers
* *
*
* *
* *
* * *
* * *
*
* * *
*
* * *
*
* *
* *
* *
* *
+
And/Or/Not Circuits (acyclic)

## Slide 62: Add 2 n-bit numbers
* *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
+
*
*
And/Or/Not Circuits (acyclic)

## Slide 63: Add 2 n-bit numbers
c1
x1 y1
+
z1
x0 y0 c0
+
z0
c2
x2 y2
+
z2
c3
x3 y3
+
z3
c4
x4 y4
+
z4
c5
x5 y5
+
z5
c5
x5 y5
+
z6
z7
With more care can be done in log n depth.
n size and n and depth.
* *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
* * *
*
+
*
*
* * *
*
And/Or/Not Circuits (acyclic)

## Slide 64
Multiplexor
r bits to be addressed
y1
yr
x1
xlogr
log r bits forms address x
yx
The addressed bit
Multiplexor
And/Or/Not Circuits (acyclic)

## Slide 65
¬x1¬x2 ¬x3 …xlogr
AND
¬x1 ¬x2 ¬x3 x4 … ¬xlogr
AND
x1 x2 ¬x3 … ¬xlogr
AND
…
Multiplexor outputs addressed bit yx.
OR
Multiplexor
All r value that might get addressed.
AND
y1
AND
yi
AND
yr
Get the bit addressed.
Circuit Size ≈ 2logr = r = size of table.
And/Or/Not Circuits (acyclic)

## Slide 66
If a TM can compute something in time T(n),
a circuit can T2(n) size and T(n) depth.
And/Or/Not Circuits (acyclic)
Some small circuit
Some small circuit
Some small circuit
Some small circuit
Some small circuit
O 00110100
H 01001000
E
01000011
L 01001101
L 01001101
qstart
O 00110100
I 01001001
E
01000011
L 01001101
L 01001101
q5

## Slide 67
And/Or/Not Circuits (acyclic)

## Slide 69
CPU
DRAM
I/O

## Slide 70
Building a CPU

## Slide 71
Clock:
5 volts/ 0 volts
open/closed
high/low
2.5 GHz = 2,500,000,000 cycles/sec
Clock
Building a CPU

## Slide 72
When clock is low, it remembers previous value.
When clock is high, new value is stored.
Memory
xt
xt
Clock
xt
xt-1
Building a CPU
xt-1
zt
yt
zt =
yt
xt
if clock=1
if clock=0
¬c
AND
OR
c
AND
xt+1
yt
cycle

## Slide 73
Building a CPU
RAM
Add *B to A
38
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC

## Slide 74
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
Multiplexor
RAM
Add *B to A
38
Add *B to A
Command

## Slide 75
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
Multiplexor
RAM
Add *B to A
38
Add *B to A
Command
38
*B

## Slide 76
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
Multiplexor
RAM
Add *B to A
38
Add *B to A
Command
38
*B
38

## Slide 77
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
Multiplexor
RAM
Add *B to A
38
Add *B to A
Command
38
*B
38
10

## Slide 78
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
RAM
Add *B to A
38
Add *B to A
Command
38
10
Add
48
New A

## Slide 79
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
RAM
Add *B to A
38
Inc
New PC
48
New A
New B
Save A to *B

## Slide 80
Building a CPU
10
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
RAM
Add *B to A
38
New PC
48
New A
New B
Save A to *B
Clock
4 8
register B

## Slide 81
Building a CPU
48
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
RAM
Add *B to A
38
Save A to *B
register B
Save A to *B
Command
Reverse Multiplexor
48

## Slide 82
Building a CPU
48
accumulator A
State of CPU & Computer at time t.
register B
program counter
PC
RAM
Add *B to A
38
Save A to *B
48
Much slower Clock

## Slide 83
Building a CPU

## Slide 84
Loader
Linker
Memory Manager
I/O Controller
Process Manager
0x3c011001
0x34240028
0x20100226
0x00004020
0x00004820
0x3c011001
0x00290821
0x8c2a0000
0x51500006
0x21290004
0x292a0028
0x1540fffa
0x3c011001
0x34240031
0x20020004
0x0000000c
0x03e00008
boolean found = false; for (int i = 0; i < 10 && !found; i++) { found = (target == list[i]); }
la $a0, yes
addi $s0, $0, 550
add $t0, $0, $0
add $t1, $0, $0
lbl: lw $t2, list($t1)
beq $t2, $s0, ok
addi $t1, $t1, 4
slti $t2, $t1, 40
bne $t2, $0, lbl
la $a0, no
ok: addi $v0, $0, 4
syscall
jr $ra

## Slide 85
Compiling Java into Machine Code

## Slide 86
Compiling Java into Machine Code
Java Model:
fancy data structures
loops
recursions
object oriented
Machine Model:
one line of simple instructions.

## Slide 87

+
exp
term
fact

fact
(
exp
)
7
term
+
term
fact
3
fact
4
(3+4)7
Compiling Java into Machine Code

## Slide 88
Algorithm: GetExp( s, i )
Exp
…
p<term,1>
p<term,2>
p<term,k>
+
+
+
A simple
recursive algorithm!

## Slide 89
Compiling Java into Machine Code

## Slide 90
boolean found = list.contains(target);
Abstract Data Types

## Slide 91
Abstract Data Types

## Slide 92: Abstract Data Types
Set: Collects a bunch of elements together.
List: A set with an order on the elements
Stack: A list, but elements can only be pushed onto and popped from the top.
Queue: A list, but elements can only be added at the end and removed from the front.
Priority Queue: The “highest priority” element is handled next.
Tree: A hierarchal structure
Graph: Edges between the elements/nodes

## Slide 93
tree
Abstract Data Types
Pointers: Store the address of more data.

## Slide 94
Abstract Data Types

## Slide 95
Thinking Abstractly About Algorithms

## Slide 96
In the beginning:
<x,y>
 <y,x mod y>
GCD(a,b) = GCD(x,y)
And so it was.
Euclid said,
“ Let there be an algorithm for GCD”
Euclid (300 BC)
Thinking Abstractly About Algorithms

## Slide 97
<preCond>
codeA
loop
<loop-invariant>
exit when <exit Cond>
codeB
codeC
<postCond>
I implored you to not worry about the entire computation.
Iterative Algorithms
9 km
5 km
A loop invariant is a statement/picture about the state of your computation to make sure it does not get lost.
Your algorithm must only maintain it while making progress

## Slide 98: Graph Search
Iterative Algorithms

## Slide 99: Recursive Algorithms
A recursive algorithm is one that calls itself.

## Slide 100: Recursive Algorithms
A recursive algorithm is one that calls itself.
X = 2133
Y = 2312
ac = 483
bd = 396
(a+b)(c+d) = 1890
XY = 4931496
X = 21
Y = 23
ac = 4
bd = 3
(a+b)(c+d) = 15
XY = 483
X = 33
Y = 12
ac = 3
bd = 6
(a+b)(c+d) = 18
XY = 396
X = 54
Y = 35
ac = 15
bd = 20
(a+b)(c+d) = 72
XY = 1890
X = 2
Y = 2
XY=4
X = 1
Y = 3
XY=3
X = 3
Y = 5
XY=15
X = 3
Y = 1
XY=3
X = 3
Y = 2
XY=6
X = 6
Y = 3
XY=18
X = 5
Y = 3
XY=15
X = 4
Y = 5
XY=20
X = 9
Y = 8
XY=72
MULT(X,Y):
If |X| = |Y| = 1 then return( XY )
Break X into a,b and Y into c,d
e = MULT(a,c) and f =MULT(b,d)
return( e 10n + (MULT(a+b, c+d) – e - f) 10n/2 + f )
I implored you to not worry about the entire computation.

## Slide 101: Recursive Algorithms
A recursive algorithm is one that calls itself.
X = 2133
Y = 2312
ac = 483
bd = 396
(a+b)(c+d) = 1890
XY = 4931496
MULT(X,Y):
If |X| = |Y| = 1 then return( XY )
Break X into a,b and Y into c,d
e = MULT(a,c) and f =MULT(b,d)
return( e 10n + (MULT(a+b, c+d) – e - f) 10n/2 + f )
You can give your “friend” any instance that is
  smaller
  meets the precondition
Trust her to give you the answer.

## Slide 102
Fourier Transformations
O(nlogn) time!
Recursive Algorithms

## Slide 103
Thinking Abstractly About Algorithms

## Slide 104
Artificial Intellegence

## Slide 105
Neural Nets

## Slide 106
Neural Nets
y
Threshold
T
x1 x2 x3 … xn
w1 w2 w3 … wn
Threshold Gate
Binary Inputs
Real Weights possibly negative
Real Threashold
Binary Output
  y = 1 iff Σi wi×xi ≥ T

## Slide 107
Neural Nets
Bicycle
Face
Wrong
Right
  The neural net learns by adjusting weights wi.
Bicycle
  The neural net learns by adjusting weights wi.
Right
  The neural net learns by adjusting weights wi.
Bicycle
Right

## Slide 108
Genetic Algorithms
Loop
Given a population of solutions.
Randomly cross two.
Keep best.

## Slide 109
Quantum Machines
What about Quantum Machines?
  A quantum TM is in the super-position of states.
  Factoring can be done in poly-time, ie 62×3.
  Not that much more.

## Slide 110
Human
What about the human brain?
  Science:
    The brain is just an elaborate machine (neural net).
  New Age:
    The brain has quantum mechanic and vibrations > machine
  Religion:
    The human has a soul >> machine

## Slide 111
Do you know the basics
of how the things in your world
work?
<x,y>
 <y,x mod y>
GCD(a,b) = GCD(x,y)
Emergent Intelligence

## Slide 112
Vision | Robotics | AI | HCI | DB | Sim | Bio | DC | QC
Areas of Study

## Slide 113: End
Notes: 113

## Slide 114
Building a Computer from Sand I will give a brief history of computing; outline the layers of abstraction within which one thinks about computing; discuss how to build an AND gate from silicon, circuits from AND gates, and a CPU from circuits; sketch how to compile a high level program into machine code; mention the basic data structures; and the paradigms of algorithms; closing with some thoughts on artificial intelligence. I don't know if there is too much here for an hour. But can stop when an hour is up.